Summary

The open source software for the Raspberry Pi RDM Controller with USB[4] is fully compatible with the Enttec USB Pro protocol[3]. The main Widget source is written in ANSI-C, and it is hardware independent.

The firmware is running on bare-metal Raspberry Pi for high precision DMX12 timing. It uses the FIQ for receiving the DMX data, and the IRQ for sending the DMX data.

The Widget is ANSI E1.11-2008 compliant (DMX512-A) and E1.20-2010 compliant (RDM).

The FT245RL USB to parallel interface is used for fast communication with the host.

The Widget configuration is stored on the sdcard. Hence the configuration is not lost when the Widget loses power.

You can also set the RDM parameters; Manufacturer name, Manufacturer id and Device label.

In the Widget mode 3, there is support for the OLA Enttec Sniffer software.

Additional to the Enttec USB Pro protocol, there is a parameter in the Widget configuration which controls the DMX receive throttling to ensure receiving software is not overloaded with too many RDM512 packets per second.

The Widget utilizes the HDMI output for displaying the real-time statistics and process information.

The Widget is extensively tested with the OLA RDM Test Server and different devices.

When using a Raspberry Pi A+ (running the firmware) and for example a Raspberry 2 Model B host with a 5V2 2A power supply, then there is no need for a powered USB hub. The Widget can directly powered from the host.

The Enttec USB Pro protocol is implemented in widget.c and in widget_usb.c
The support for the OLA Enttec Sniffer software is implemented in widget_sniffer.c
The output for the external HDMI monitor is implemented in widget_monitor.c
The support for saving the Widget configuration is implemented in widget_params.c

More information can be found here http://www.raspberrypi-dmx.com/raspberry-pi-rdm-controller

The complete open source can be found here https://github.com/vanvught/rpidmx512/tree/master/rpi_dmx_usb_pro

The hardware is available from here http://www.bitwizard.nl/shop/index.php?route=product/product&product_id=154

Introduction

This document describes the open source Raspberry Pi RDM Controller with USB, DMX512 isolated board and compatiblitiy with software that supports Enttec USB Pro.

Main features

- Raspberry Pi baremetal programming controls DMX512 / RDM timing
- Open source https://github.com/vanvught/rpidmx512/tree/master/rpi_dmx_usb_pro
- Supported operating systems: Windows, MAC OS, Linux
- Using the FT245RL USB to parallel interface for fast communication with the host
- DMX512 Transmitter or Receiver
- No external power supply required
- ANSI E1.11-2008 compliant (DMX512-A)
- E1.20-2010 compliant (RDM)
- Fully compatible with software suitable for ENTTEC USB Pro[2]
- Configuration is stored on the sdcard (file "params.txt")
- Set your own manufacturer name and id (file "rdm_device.txt")
- Compatible with OpenLighting rdmpro_sniffer[3] (widget_mode=3)
- DMX receive rate throttling option to ensure receiving software isn't overloaded with too many frames per second
- Real-time statistics and process information is available on external monitor
- UUID (or S/N) is based on MAC-address (works across all Raspberry Pi models)

Configuration

The Widget configuration is stored on the sdcard in the file "params.txt".

Widget Parameter	Description	Default
dmxusbpro_break_time	DMX output break time in 10.67 microsecond units. Valid range is 9 to 127.	9
dmxusbpro_mab_time	DMX output Mark After Break time in 10.67 microsecond units. Valid range is 1 to 127.	1
dmxusbpro_refresh_rate	DMX output rate in packets per second. Valid range is 1 to 40, or 0 for fastest rate possible.	40
dmx_send_to_host_throttle	DMX receive rate throttling option in updates per second. 0 is as fast as possible.	0
widget_mode	The widget mode. See table “Widget mode“ for the supported values	2

Tabel 1: params.txt

Value	Description
0	Mode 1 + 2
1	Normal DMX firmware. Supports all messages except Send RDM (label=7), Send RDM Discovery Request(label=11) and receive RDM
2	RDM firmware. This enables the Widget to act as an RDM Controller.
3	RDM Sniffer firmware. This is for use with the Openlighting RDM packet monitoring application[3].

Tabel 2: Widget mode

Example :
#dmxusbpro_break_time=
#dmxusbpro_mab_time=
#dmxusbpro_refresh_rate=0
widget_mode=0
#dmx_send_to_host_throttle=20

The RDM device configuration is stored on the sdcard in the file "rdm_device.txt".

Name	Description	Label
manufacturer_name	Manufacturer Name (maximum length is 32 characters) .	77
manufacturer_id	Manufacturer ID : http://tsp.plasa.org/tsp/working_groups/CP/mfctrIDs.php
device_label	Descriptive label for the device (maximum length is 32 characters).	78

Tabel 3: rdm_device.txt
Example:
manufacturer_name=Open Lighting
#manufacturer_id=7A70
#device_label=

Software

Init functions	Source file	Library
hardware_init	hardware.c	hal
usb_init	usb.c	hal
dmx_init	dmx.c	n.a.
widget_params_init	widget_params.c	n.a.
rdm_device_info_init	rdm_device_info.c	n.a.

Tabel 4: Init functions in main.c

Function	Source file
widget_receive_data_from_host	widget.c
widget_received_dmx_packet	widget.c
widget_received_rdm_packet	widget.c
widget_rdm_timeout	widget.c
widget_sniffer_rdm	widget_sniffer.c
widget_sniffer_dmx	widget_sniffer.c

Tabel 5: Poll table in main.c

Function	Source file	Time
monitor_update	widget_monitor.c	1 sec

Tabel 6: Event table in main.c

PL011

The BCM2835 device has two UARTS. One mini UART and one PL011 UART. The PL011 UART is used for the DMX protocol support.

The UART clock rate is set to 4Mhz using the VideoCore mailbox function: bcm2835_vc_set_clock_rate(BCM2835_VC_CLOCK_ID_UART, 4000000)

With a 4Mhz UART clock rate the Integer Baud Rate Divisor register (IBRD) is to 1 (4000000 / (16 * 250000)), and the Fractional Baud Rate Divisor register (FBRD) is set to 0.

The Line Control Register (LCRH) is set to PL011_LCRH_WLEN8 | PL011_LCRH_STP2. That is parity is disabled and no parity bit added to the data frame, two stop bits are transmitted at the end of
the frame, FIFOs are disabled (character mode) that is, the FIFOs become 1-byte-deep holding registers and 8 bits of data is transmitted or received in a frame.

The complete PL011 initiation can be found in function static void pl011_init(void).

Hardware

PL011

RPi / P1	SoC / Broadcom	Description	FSEL
8	GPIO14	PL011 TXD	ALT0
10	GPIO15	PL011 RXD	ALT0

Tabel 7: PL011

RPi / P1	SoC / Broadcom	Description	FSEL
12	GPIO18	0 = input / 1 = output	OUTP

Tabel 8: DMX data direction GPIO

The FT245RL USB to parallel interface is used for fast communication with the host. Table \ref{table:ft245rl} refers to the connection details.
The 8 bits data for reading from the USB is available from bcm2835 register GPLEV0. The data is read as follows:

Hence it is save to write 32-bits to bcm2835 register GPSET0. Quote from [1] `The SET{n} field defines the respective GPIO pin to set, writing a “0” to the field has no effect. If the GPIO pin is being used as in input (by default) then the value in the SET{n} field is ignored.' The same applies for writing to the bcm2835 register GPCLR0. Quote from the [1] : `The CLR{n} field defines the respective GPIO pin to clear, writing a “0” to the field has no effect.'

RPi / P1	SoC / Broadcom		USB / FT245RL
3	GPIO02		D0
5	GPIO03		D1
7	GPIO04		D2
26	GPIO07		D3
24	GPIO08		D4
21	GPIO09		D5
19	GPIO10		D6
23	GPIO11		D7
15	GPIO22		WR
16	GPIO23		RD
18	GPIO24		TXE
22	GPIO25		RXF

Tabel 9: FT245RL-GPIO

References
1. Broadcom, BCM2835 ARM Peripherals, pdf (errata)
2. DMX USB Pro Widget API Specification 1.44, pdf
3. Openlighting RDM packet monitoring
4. DMX interface for Raspberry Pi with USB (FT245RL), link