Introduction

This document describes the Open source Raspberry Pi RDM Controller with USB, DMX512 isolated board and compatible with software that supports Enttec USB Pro.

Main features

- Raspberry Pi baremetal programming controls DMX512 / RDM timing
- Open source https://github.com/vanvught/rpidmx512/tree/master/rpi_dmx_usb_pro
- Supported operating systems: Windows, MAC OS, Linux
- Using the FT245RL USB to parallel interface for fast communication with the host
- DMX512 Transmitter or Receiver
- No external power supply required
- ANSI E1.11-2008 compliant (DMX512-A)
- E1.20-2010 compliant (RDM)
- Fully compatible with software suitable for ENTTEC USB Pro
- Configuration is stored on the sdcard (file "params.txt")
- Set your own manufacturer name and id (file "rdm_device.txt")
- Compatible with OpenLighting rdmpro_sniffer (widget_mode=3)
- DMX receive rate throttling option to ensure receiving software isn't overloaded with too many frames per second
- Real-time statistics and process information is available on external monitor
- UUID (or S/N) is based on MAC-address (works across all Raspberry Pi models)

Configuration

The Widget configuration is stored on the sdcard in the file "params.txt".

Widget Parameter	Description
dmxusbpro_break_time	DMX output break time in 10.67 microsecond units. Valid range is 9 to 127 (default = 9).
dmxusbpro_mab_time	DMX output Mark After Break time in 10.67 microsecond units. Valid range is 1 to 127 (default = 1).
dmxusbpro_refresh_rate	DMX output rate in packets per second. Valid range is 1 to 40, or 0 for fastest rate possible (default = 40).
dmx_send_to_host_throttle	DMX receive rate throttling option in updates per second. 0 is as fast as possible (default = 0).
widget_mode	The widget mode. See table “Widget mode“ for the supported values

Tabel 1: params.txt

Value	Description
0	Mode 1 + 2
1	Normal DMX firmware. Supports all messages except Send RDM (label=7), Send RDM Discovery Request(label=11) and receive RDM
2	RDM firmware. This enables the Widget to act as an RDM Controller. (default)
3	RDM Sniffer firmware. This is for use with the Openlighting RDM packet monitoring application.

Tabel 2: Widget mode

Example :
#dmxusbpro_break_time=
#dmxusbpro_mab_time=
#dmxusbpro_refresh_rate=0
widget_mode=0
#dmx_send_to_host_throttle=20

The RDM device configuration is stored on the sdcard in the file "rdm_device.txt".

Name	Description
manufacturer_name	Manufacturer Name (maximum length is 32 characters) Widget Label = 77
manufacturer_id	Manufacturer ID : http://tsp.plasa.org/tsp/working_groups/CP/mfctrIDs.php
device_label	Descriptive label for the device (maximum length is 32 characters). Widget Label = 78

Tabel 3: rdm_device.txt
Example:
manufacturer_name=Open Lighting
#manufacturer_id=7A70
#device_label=

Hardware

The FT245RL USB to parallel interface is used for fast communication with the host. Table \ref{table:ft245rl} refers to the connection details.
The 8 bits data for reading from the USB is available from bcm2835 register GPLEV0. The data is read as follows:

Hence it is save to write 32-bits to bcm2835 register GPSET0. Quote from the `BCM2835-ARM-Peripherals.pdf` : `The SET{n} field defines the respective GPIO pin to set, writing a “0” to the field has no effect. If the GPIO pin is being used as in input (by default) then the value in the SET{n} field is ignored.' The same applies for writing to the bcm2835 register GPCLR0. Quote from the `BCM2835-ARM-Peripherals.pdf` : `The CLR{n} field defines the respective GPIO pin to clear, writing a “0” to the field has no effect.'

RPi / P1	SoC / Broadcom		USB / FT245RL
3	GPIO02		D0
5	GPIO03		D1
7	GPIO04		D2
26	GPIO07		D3
24	GPIO08		D4
21	GPIO09		D5
19	GPIO10		D6
23	GPIO11		D7
15	GPIO22		WR
16	GPIO23		RD
18	GPIO24		TXE
22	GPIO25		RXF

Tabel 4: FT245RL-GPIO